## Slide 1: OBSERVING THE RELATIONSHIP BETWEEN VOLTAGE AND CURRENT WITH HIGH POWERED LASERS UNDER DIFFERENT TEMPERATURES
By: Natalie Caro
Data Collected by: Aditi Patel & Natalie Caro
May 6, 2019

## Slide 2: Outline
Introduction
Optical layout
Data
Results
Conclusion
References

## Slide 3: Introduction
Laser: Light Amplification by Stimulated Emission of Radiation
Has only one wavelength, moves in one direction, and is monochromatic.
Lasers are in use everywhere:
  DVDs
  Cutting steel in factories
  Scanning labels in supermarkets
  Performing surgery in hospitals
Solid-state lasers are lasers whose outputs range in wave- length from roughly 170 nm to 3900 nm.

## Slide 4: Optical Layout

## Slide 5: Data with and without Nd filter
Chart: Current Vs Voltage
| 90.8 | 150.30000000000001 | 210.1 | 270.10000000000002 | 330 | 390.8 | 450 | 510.7 | 570 | 630.5 | 690.1 | 750.1 | 810 | 870 | 930.3 | 990.2 | 1050.2 | 1110.4000000000001 | 1180.2 | 1280 | 1380.2 | 1480 | 1580 | 1680 | 1780 | 1880 | 1980 | 2000
no ND filter | 0 | 0.001 | 0.002 | 0.004 | 0.007 | 0.015 | 0.039 | 0.146 | 0.544 | 0.586 | 0.602 | 0.609 | 0.612 | 0.613 | 0.615 | 0.617 | 0.618 | 0.619 | 0.618 | 0.618 | 0.618 | 0.618 | 0.618 | 0.618 | 0.618 | 0.618 | 0.618 | 0.618
2.8 ND filter | 0 | 0.001 | 0.006 | 0.015 | 0.027 | 0.038 | 0.05 | 0.066 | 0.086 | 0.101 | 0.12 | 0.135 | 0.156 | 0.184 | 0.193 | 0.219 | 0.245 | 0.268 | 0.29 | 0.315 | 0.35 | 0.369 | 0.37 | 0.39 | 0.403 | 0.422 | 0.427 | 0.43 | 0.429
Current Threshold: 500mA
Saturation from detector: 0.6V
The ND filter made it possible to measure the gradual increase from the current threshold to the level of saturation.
Current threshold

## Slide 6: Data Time vs temperature
Chart: Time vs Temperature
| 0 | 30 | 60 | 90 | 120 | 150 | 180 | 210 | 240 | 270 | 300
Temperature (F) | 46.2222 | 59.2222 | 73.2222 | 87.2222 | 98.2222 | 110.2222 | 117.2222 | 114.2222 | 113.2222 | 124.2222 | 132.2222
Styrofoam
Current is at a constant 2000mA.
Recorded temperature every 30s for 300s
Temperature increases the longer the laser is on.

## Slide 7: Data Time vs voltage
Chart: Time vs Voltage
| 0 | 30 | 60 | 90 | 120 | 150 | 180 | 210 | 240 | 270 | 300
Voltage (V) | 0.204 | 0.201 | 0.183 | 0.173 | 0.161 | 0.166 | 0.181 | 0.174 | 0.155 | 0.123 | 0.075
Current is at a constant 2000mA.
Recorded laser power every 30s for 300s
Power decreases the longer the laser is on.

## Slide 8: Results Temperature vs Power
Chart: Temperature vs Power
| 46.222222222222221 | 59.222222222222221 | 73.222222222222229 | 87.222222222222229 | 98.222222222222229 | 110.22222222222223 | 117.22222222222223 | 114.22222222222223 | 113.22222222222223 | 124.22222222222223 | 132.22222222222223
Voltage (V) | 0.204 | 0.201 | 0.183 | 0.173 | 0.161 | 0.166 | 0.181 | 0.174 | 0.155 | 0.123 | 0.075
Combined previous two graphs
Power does decrease as temperature increases
Error

## Slide 9: Results Differences of thermal stability
Chart: Current vs Voltage
| 480 | 530.79999999999995 | 580.5 | 630 | 680.9 | 730.2 | 780.3 | 830.7 | 880.4 | 930.6 | 980.2 | 1030 | 1080.5999999999999 | 1130.5999999999999 | 1180.3 | 1230.0999999999999 | 1280.9000000000001 | 1330.4 | 1380.5 | 1430.1 | 1480.4 | 1530.7 | 1580.5 | 1630.9 | 1680.9 | 1780.8 | 1880.7 | 1980.7 | 2000
Temp 22C | 0 | 0.001 | 0.006 | 0.015 | 0.027 | 0.038 | 0.05 | 0.066 | 0.086 | 0.101 | 0.12 | 0.135 | 0.156 | 0.184 | 0.193 | 0.219 | 0.245 | 0.268 | 0.29 | 0.315 | 0.35 | 0.369 | 0.37 | 0.39 | 0.403 | 0.422 | 0.427 | 0.43 | 0.429
Temp 45C | 0.326 | 0.253 | 0.232 | 0.198 | 0.17 | 0.136 | 0.107 | 0.079 | 0.057 | 0.027 | 0.009
Temp 45C no voltage | 0 | 0 | 0 | 0 | 0
Set the laser to 45C
Current Threshold: 1000mA
The overall voltage is weaker at a higher temperature than with a cooler temperature.
Current threshold
Current threshold
T=22C
T=45C

## Slide 10: Results waveform generator
Waveform Generator is connected to the oscilloscope on Channel 1
Laser Diode Driver is connected on Channel 2
Frequency at 5.6Hz the waves are synchronized
Frequency at 50.6Hz the waves are beginning to distort
Frequency at 150.6Hz the waves are no longer in synch.
There is limit to what the detector can receive.

## Slide 11: Conclusion
Errors
  Fluctuating multimeter
  Inaccurate readings from working quickly
  Fluctuating temperature
High temperature does lower laser power
How to fix/improve: heat sinks, liquid cooling, air cooling.

## Slide 12: References
[1] Ab-Rahman, M. (2012). The Effect of Temperature on the Performance of Uncooled Semiconductor Laser Diode in Optical Network. Journal of Computer Science,8(1), 84-88. doi:10.3844/jcssp.2012.84.88
[2] Pankove, J. I. (1968). Temperature Dependence of Emission Efficiency and Lasing Thresholds in Laser Diodes. Journal of Quantum Electronics, 4, 4th ser., 119-122.

## Slide 13: Thank you for your attention
If you have any further questions, please reach out to me at
nlc4@njit.edu